## Slide 1: Sensors
Color Identification
Mike Zook 13-Sep-2016

## Slide 2: Training Objectives
Color is described in 3 coordinates.
RGB and HSV color coordinates are provided by the FTC Robot App.
Many variables affect color measurement.
To promote accuracy, keep measurement conditions stable.

## Slide 3: Color Coordinates
Color is typically defined in 3 coordinates
Common color coordinate types:
  RGB – Red, Green, Blue
  HSV – Hue Saturation Value
  HSI – Hue, Saturation, Intensity
Each type has advantages depending upon the application.
The FTC Robot Controller app provides RGB by default and a method to convert RGB to HSV

## Slide 4: RGB Coordinates
Green
Blue
Red

## Slide 5: HSV Coordinates
Value
Saturation
Hue
Hue (0 to 360 degrees)
Saturation (% or count)
Value (% or count)

## Slide 6: Mr. Zook’s Recommendation
Use HSV instead of RGB to identify line and beacon colors
Why? Because ….

## Slide 7: Color Training
White
Establish relevant coordinate limits
Examples:
  Blue
    min blue hue < H < max blue high
    S > min blue saturation
    V > min blue value
  Red
    min red hue > H, or H < max red hue
    S > min red saturation
    V > min rd value
  White
    saturation < [colorful]
    value > [dark]
Value
Saturation
Hue

## Slide 8: Color Measurement
Color measurements are impacted by many variables including but not limited to:
    proximity of sensor to object
    light intensity and color
        ambient
        machine vision light source
    lens filters (color, polarity)
    noise (e.g., particulates, foreign objects)
Limit variables to improve measurement repeatability and accuracy!
    Maintain sensor distance
    Keep sensor distance short
    Block foreign light sources

## Slide 9: Sensor Setup
Sensor Outputs: RGB, Brightness, and many more (refer to color sensor specs for all outputs)
Lighting
    Supplemental white light needed to differentiate field lines
    Block all/most ambient light to identify beacon colors
Modern Robotics Device Interface Module
  IC2 Channel – color measurements
  DO Channel – White LED power/control
  CAUTION – Each IC2 sensor must have a unique address

## Slide 10: Greenwood Challenge
Create methods to identify line and beacon color.
  Examples:
    lineColor – returns red, blue, white, none
    lineWhite – returns true or false
    lineRed – returns true or false
    beaconBlue – returns true or false
Create line following method.
  Example:
    Turn left if line detected.
    Turn right if line lost.
    Turn off if line lost for excessive time.