## Slide 1: Sensors
Quadrature Encoders
Mike Zook 30-Aug-2016

## Slide 2: Training Objectives
Encoders are used to track position
Three modes of control:
    Torque
    Speed
    Target
Math is your friend
Match motor outputs to encoder inputs

## Slide 3: Encoders
Purpose: Track position and speed
Types and technologies:
  Mechanical, optical, magnetic, etc.
  Linear and rotary
  Absolute and Incremental
    Absolute encoders – true position
    Incremental encoders – cycling outputs
We will use Quadrature Encoders (incremental encoder variety)

## Slide 4: Quadrature Encoders
Two pulsing outputs (channels a and b)
Outputs are 90 degrees out of phase
Each output transition indicates …
  incremental change in position
  direction of movement
A third indexing output (channel z) may be included to flag motor “home” position.

## Slide 5: Quadrature Encoders
Same Signal Shape (square wave), but
90 degrees out of phase.

## Slide 6: Quadrature Encoders
FORWARD MOTION |  |  |  |  |  |  |  |  |  | 
a | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
b | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
REVERSE MOTION |  |  |  |  |  |  |  |  |  | 
a | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
b | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
time
time

## Slide 7: The Easy Part
Do not worry about decoding the signals; the motor ‘commands’ will do the work for you!
Define motion type
  Torque,
  Velocity, or
  Position (go to target)
    By default, all moves are absolute
    Target Position units are “encoder counts”
    Need to set Velocity too for position moves

## Slide 8: FTC Robot Controller Motor Modes
RESET_ENCODER – sets current motor position to zero
RUN_WITHOUT_ENCODER
  Torque motion type
  “setPower” adjusts torque output
RUN_USING_ENCODER
  Speed motion type; torque adjusted automatically
  “setPower” adjusts motor speed
RUN_TO_POSITION
  Position motion type
  “setTargetPosition” used to define destination (absolute)
  “setPower” adjusts motor speed; torque adjusted automatically

## Slide 9: Absolute vs. Relative Moves
Go 8, Go 4, Go -7, Go 5

## Slide 10: The Math Part
What is the relationship between encoder counts and distance travelled?
f(x) = GR · [RECR / Wcir] · x
Given:
f(x) = Distance [encoder counts]
x = Distance [engineering units]
RECR = Encoder Counts per Revolution [counts/rev.]
GR = Gear Ratio
Wcir = Wheel Circumference [engineering units] = 2r π

## Slide 11: The Math Part - Example
How many counts are needed to travel 24 inches if wheel radius is 1.5 inches, gear ratio is 2:1, and a 1000 count/rev encoder installed?
f(x) = GR · [RECR / Wcir] · x
= 2 · (1000/9.4) · 24
= 5106 counts
Given:
f(x) = Distance [encoder counts]
x = Distance [engineering units] = 24 inches
RECR = Encoder Counts per Rev. [counts/rev.] = 1000
GR = Gear Ratio = 2
Wcir = Wheel Circumference [engineering units] = 2r π
= 2 x 1.5 inches x π = 9.4 inches

## Slide 12: Core Motor Controller
Illustration by Modern Robotics

## Slide 13: Training Objectives
Encoders are used to track position
Three modes of control:
    Torque
    Speed
    Target
Math is your friend
Match motor outputs to encoder inputs